## Slide 1
By Ibrahim siraj
Maldives polytechnic
CERTIFICATE III IN AUTOMOTIVE REPAIR & MAINTENANCE
SUBJECT: Automotive Engineering Workshop

## Slide 2
Chapter 1 Applications of Petrol and Diesel Engines
Internal combustion (IC) engines convert chemical energy in fuel into mechanical work.
Two main types:
  Petrol (Gasoline) Engines
  Diesel Engines
Both are widely used in transportation, power generation, and industrial applications.
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 3
Chapter 1 Applications of Petrol and Diesel Engines
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 4
Chapter 1 Applications of Petrol and Diesel Engines
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Otto A theoretical model that describes the functioning of a spark-ignition internal combustion engine, commonly known as a four-stroke engine.
thermodynamic model of a four-stroke internal combustion engine that uses compression to ignite fuel, not a spark plug.

## Slide 5
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
The Four-Stroke Cycle
Most modern engines operate on a Four-Stroke Cycle, discovered by Nikolaus Otto (1876).
The four strokes are:
1- Intake (Suction) Stroke
2- Compression Stroke
3- Power (Expansion) Stroke
4- Exhaust Stroke

## Slide 6
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
1. Intake (Suction) Stroke
Piston moves downward.
Inlet valve opens, exhaust valve closes.
Air-fuel mixture (in petrol engine) or air (in diesel engine) enters the cylinder.
Objective: Fill cylinder with charge for combustion.

## Slide 7
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
2. Compression Stroke
Both valves closed.
Piston moves upward, compressing the mixture (or air).
Compression increases pressure and temperature inside the cylinder.
At the end of this stroke:
  Petrol Engine: Spark plug ignites the mixture.
  Diesel Engine: Fuel is injected and ignites due to heat of compression.

## Slide 8
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
3. Power (Expansion) Stroke
Combustion occurs, producing high-pressure gases.
The expanding gases push the piston downward.
This is the only stroke that produces power.
Crankshaft converts this movement into rotational energy.

## Slide 9
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
4. Exhaust Stroke
Exhaust valve opens, inlet valve closes.
Piston moves upward, pushing out the burnt gases.
Cylinder becomes ready for the next cycle.

## Slide 10
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Two-Stroke Engine Principle (Optional Slide)
In a two-stroke engine, all four operations occur in two piston strokes (one revolution of crankshaft).
Advantages: Simple design, lightweight, more power for size.
Used in: Motorbikes, scooters, chainsaws.
Disadvantages: Less fuel efficient, more pollution

## Slide 11
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Two-Stroke Engine Principle (Optional Slide)

## Slide 12
Chapter 1 Applications of Petrol and Diesel Engines Basic Working Principle
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 13
Chapter 1 Applications of Petrol and Diesel Engines
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Feature | Petrol Engine | Diesel Engine
Fuel | Petrol (Gasoline) | Diesel
Ignition | Spark Ignition (SI) | Compression Ignition (CI)
Compression Ratio | Low (6:1 to 10:1) | High (14:1 to 22:1)
Efficiency | Lower | Higher
Maintenance | Lower | Higher
Basic Difference Between Petrol and Diesel Engines
A compression ratio is the measure of the maximum cylinder volume (piston at bottom) compared to the minimum volume (piston at top) in an engine

## Slide 14
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Automobiles:
Cars, motorbikes, scooters, and small trucks.
Popular for light-duty vehicles due to smooth and quiet operation.
Small Machinery:
Lawn mowers, chainsaws, generators, and portable pumps.
Aviation (Light Aircraft):
Used in small aircraft with piston engines
Marine:
Small boats and jet skis where compactness and low vibration are preferred
Applications of Petrol Engines

## Slide 15
Chapter 1 Applications of Petrol and Diesel Engines
Applications of Diesel Engines
1. Heavy-Duty Transport:
Trucks, buses, tractors, and lorries use diesel for high torque and fuel efficiency.
2. Power Generation:
Diesel generator sets (DG sets) for electricity backup and remote power supply.
3. Marine Applications:
Large ships, cargo vessels, and submarines rely on diesel engines.
4. Industrial Equipment:
Excavators, cranes, compressors, and mining equipment.
5. Locomotives:
Diesel-electric locomotives for rail transport.
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 16
Chapter 1 Applications of Petrol and Diesel Engines
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic
Petrol Engine | Diesel Engine
Smooth, quiet operation | Better fuel economy
Easy starting, especially in cold weather | Higher torque and power for heavy loads
Lower initial cost | Longer lifespan
Lightweight | More durable under high load
Comparative Advantages

## Slide 17
Chapter 1 Applications of Petrol and Diesel Engines
Environmental Considerations
Petrol Engines: Emit more CO2 and unburned hydrocarbons.
Diesel Engines: Produce more NOx and particulates but less CO2.
Both are being improved with turbocharging, fuel injection, and emission control systems.
Particulate Matter (PM)
Hydrocarbons + Nitrogen Oxides
Nitrogen Oxides
Hydrocarbons
Carbon monoxide
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 18
Chapter 1 Applications of Petrol and Diesel Engines
Future Trends
Hybrid systems (petrol-electric and diesel-electric).
Cleaner fuels and biodiesel.
Advancements in emission reduction (e.g., catalytic converters, SCR).
Shift toward electric mobility
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 19
Chapter 1 Applications of Petrol and Diesel Engines
Conclusion
Both petrol and diesel engines play vital roles in modern life.
Petrol engines dominate light vehicles and portable machinery.
Diesel engines are preferred for heavy-duty and industrial applications.
Continuous innovations aim to make both more efficient and eco-friendly
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 20
Chapter 1 Applications of Petrol and Diesel Engines
References
Textbooks on IC Engines (e.g., V. Ganesan, M.L. Mathur & R.P. Sharma)
Manufacturer websites (Cummins, Caterpillar, Honda, Toyota)
Government and automotive energy reports
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 21
Chapter 1 Applications of Petrol and Diesel Engines
References
Textbooks on IC Engines (e.g., V. Ganesan, M.L. Mathur & R.P. Sharma)
Manufacturer websites (Cummins, Caterpillar, Honda, Toyota)
Government and automotive energy reports
Automotive Engineering Practice
By Ibrahim siraj
Maldives polytechnic

## Slide 22
THANK YOU